# Section 1: Selected Response
Directions: Place the letter that corresponds to the correct answer on the space provided.

___ 1. What component in the ignition system steps up voltage?
1. battery
2. powertrain control module (computer)
3. ignition coil
4. spark plug

___ 2. What type of grease is used in spark plug boot ends to inhibit corrosion?
1. dielectric
2. chassis
3. anti-seize
4. white lithium

___ 3. Most automobiles have a ______ volt DC battery.
1. 2
2. 6
3. 12
4. 120

___ 4. In a distributor ignition system, what rotates under the distributor cap to send the high voltage to each spark plug wire?
1. rotator
2. rotor
3. ring
4. rasp

___ 5. Some electronic ignition systems eliminate the use of spark plug wires. What do they use to do this?
1. distributor cap
2. distributor rotor
3. coil-on-plug
4. ignition coils

___ 6. What would be a reasonable gap setting for a spark plug?
1. 0.0040” (0.1016 mm)
2. 0.040” (1.016 mm)
3. 0.400” (10.16 mm)
4. 4.000” (101.6 mm)

___ 7. What would be a reasonable voltage at the tip of a spark plug?
1. 5 volts
2. 500 volts
3. 50,000 volts
4. 500,000 volts
___ 8. What component in the suspension system combines the shock, spring, and upper control arm into one unit?
1. tire
2. leaf spring
3. strut
4. coil spring

___ 9. What type of steering system has a pitman arm?
1. parallelogram system
2. rack and pinion system
3. tie rod system
4. power steering system

___ 10. What does the P stand for in P205/55R16 89H?
1. pressure
2. psi
3. pounds
4. passenger

___ 11. What is used to reduce the amount of effort needed to turn the steering wheel?
1. power steering
2. shock
3. strut
4. tie rod

___ 12. Which of the following is the best UTQG rating for traction?
1. AA
2. A
3. B
4. C

___ 13. At what distance are wear indicator bars set?
1. 2/32” (1.6 mm); simplified as 1/16”
2. 16/32” (12.7 mm); simplified as ½”
3. 32/32” (25.4 mm); simplified as 1”
4. 48/32” (38.1 mm); simplified as 1.5”

___ 14. What type of pattern should be used when tightening lug nuts?
1. circular
2. star
3. square
4. rectangular
  Section 2: Selected Response ASE Style Questions
Directions: Place the letter that corresponds to the correct answer on the space provided.

___ 15. Technician A says that most new cars have electronic ignition systems. Technician B says that crankshaft and camshaft sensors are used with electronic ignition systems. Who is correct?
1. Technician A
2. Technician B
3. Both Technician A and Technician B
4. Neither Technician A nor Technician B

___ 16. Technician A says that most car batteries are 6 volts. Technician B says that about 50% of new cars have 6 volt systems while 50% have 12 volt systems. Who is correct?
1. Technician A
2. Technician B
3. Both Technician A and Technician B
4. Neither Technician A nor Technician B

___ 17. Technician A says that all automobiles only have one ignition coil. Technician B says that some automobiles have one coil per cylinder. Who is correct?
1. Technician A
2. Technician B
3. Both Technician A and Technician B
4. Neither Technician A nor Technician B

___ 18. Technician A says that diesel engines do not have spark plugs. Technician B says that diesel engines use two spark plugs for each cylinder due to the high energy content of the diesel fuel. Who is correct?
1. Technician A
2. Technician B
3. Both Technician A and Technician B
4. Neither Technician A nor Technician B

___ 19. Technician A says that when changing the spark plug wires on a distributor ignition vehicle it is essential not to mix up the firing order. Technician B says that it is important to route the wires away from the exhaust manifold to prevent the wires from burning. Who is correct?
1. Technician A
2. Technician B
3. Both Technician A and Technician B
4. Neither Technician A nor Technician B

___ 20. Technician A says that correct tire pressure is critical to tire wear and vehicle handing. Technician B says that a tire pressure monitoring system is used to alert the driver if any tire is significantly low on pressure. Who is correct?
1. Technician A
2. Technician B
3. Both Technician A and Technician B
4. Neither Technician A nor Technician B

___ 21. Technician A says that a “V” speed rated tire has met higher speed standards than a “T” speed rated tire. Technician B says that an “H” speed rated tire has a higher speed rating than both “V” and “T” speed rated tires. Who is correct?
1. Technician A
2. Technician B
3. Both Technician A and Technician B
4. Neither Technician A nor Technician B

___ 22. Technician A says that most front wheel drive vehicles use parallelogram steering systems. Technician B says that an idler arm is used with rack and pinion steering systems. Who is correct?
1. Technician A
2. Technician B
3. Both Technician A and Technician B
4. Neither Technician A nor Technician B

___ 23. Technician A says that a “C” load range tire has more tire plies than a “D” load range tire. Technician B says that an “E” load range tire has more tire plies than a “C” or a “D”. Who is correct?
1. Technician A
2. Technician B
3. Both Technician A and Technician B
4. Neither Technician A nor Technician B

___ 24. Technician A says that when inflating tires, you should check the tire placard for the correct recommended pressure. Technician B says that you can tell when a tire is fully inflated by looking at it. Who is correct?
1. Technician A
2. Technician B
3. Both Technician A and Technician B
4. Neither Technician A nor Technician B